ALUMINUM INTERIOR PASS WINDOW ASSEMBLIES

SECTION 08 56 19

# PART 1 – GENERAL

1.01	 SUMMARY

- This section includes:

- Aluminum, medium-duty interior sliding pass window assemblies as indicated in drawings and in sections.

1.02 		RELATED REQUIREMENTS

A.	Section 08 80 00 - Glazing

B.	Section 12 35 00 - Specialty Casework

1.03 	SUBMITTALS

- Product Data: Submit Manufacturer’s technical product data substantiating that product complies.

- Shop drawings: Submit for fabrication and installation of windows. Include details, elevations and installation requirement of finish hardware and cleaning.

1.04 	DELIVERY, STORAGE, AND HANDLING

- Deliver components with adequate protection to prevent damage during transit and job storage

- Inspect components upon delivery for damage. Unless minor defects can be made to meet the Architect’s specifications and satisfaction, damaged parts should be removed and replaced.

- Store components at building site under cover in dry location.

1.05 	PROJECT CONDITIONS

- Field measurements: Check opening by accurate field measurement before fabrication. Show recorded measurements on shop drawings. Coordinate fabrication schedule with construction progress to avoid delay of work.

1.06	QUALITY ASSURANCE

A.	Installer qualifications: Engage an experienced installer who has completed 	installations of Interior Sliding Pass Window Assemblies similar in design and 	extent to those required for the project and whose work has resulted in 	construction with a record of success in service performance.

B.	Manufacturer’s qualifications: Sliding Pass Window Assembly produced by a 	firm experienced in manufacturing Interior Sliding Pass Windows that are similar 	to those indicated for this project and that have a record of success in service 	performance.

C.	Single source responsibility: Obtain Sliding Pass Window Assembly from a single 	manufacturer to ensure full compatibility and warranty of parts.

D.	Design criteria: The drawings indicate the size, profile and dimensional 	requirements of the Sliding Pass Window Assembly required and are based on the 	specific types and models indicated.

E.	Safety glass standards: (By Others)

1. 	Tempered glass components that comply with ANSI Z97.1

# PART 2 - PRODUCTS

2.01 	ACCEPTABLE MANUFACTURER’S

- Basis of design: Design is based on aluminum, interior sliding pass window assembly manufactured by:

C.R. Laurence Co., Inc. (CRL)

Tel: (800) 421-6144 Ext. 7760 Fax: (800) 458-7496

Email: transaction@crlaurence.com

www.crlaurence.com

2.02 	MATERIALS

- Frames: Aluminum frame modules shall be constructed of 6063-T5 extruded aluminum.  Assemblies roll on base shoes with rollers engaged in lower track. Jambs are optional and must be specified if desired.

- Finish: All aluminum to be clear anodized, duranodic bronze, or for selected models, brushed nickel or flat black.

- Glazing: Typically 1/4” (6 mm) in thickness. Glass not included, to be supplied by others.

- Options: Keyed lock, finger pulls, end caps, and selected models have anti-lift security features.

- Pass Window Assembly Models: (Architect to Specify)

1. D2301

2. D2307

3. D2300

4. D2203

5. D2204

6. CTA00

7. S700

PART 3 – EXECUTION

3.01	 INSTALLATION

- Install components in accordance with manufacturer’s printed instructions and recommendations. Repair damaged units as directed (if approved by the manufacturer and the architect) or replace with new units.

3.02 	CLEANING

A.	Clean frame and glazing surfaces after installation, complying with requirements contained in the manufacturer’s instructions. Remove excess glazing sealant compounds, dirt or other substances.

3.03 	PROTECTION

A.	Institute protective measures required throughout the remainder of the construction period to ensure that all the windows do not incur any damage or deterioration, other than normal weathering, at the time of acceptance.

## END OF SECTION